## Slide 1
Latency biases in nonparametric permutation tests for electrophysiological EEG/MEG data

## Slide 2
“The analysis of functional mapping experiments in positron emission tomography and fMRI involves the formation and assessment of images of statistics. Existing methods are predominantly parametric, requiring a multitude of assumptions and relying on various approximations.”

## Slide 3
Nichols & Holmes, HBM, 2001
Suppose that conditions Active A and Rest B were presented alternately and that
the observed ABABAB data at one voxel are {103.00; 90.48; 99.93, 87.83, 99.76, 96.06}
= 9.45
The T-value for ABABAB is the highest of all
20 permutations, thus p = 1/20 = 0.05

## Slide 4
Nichols & Holmes, HBM, 2001
With alpha=0-05 and 1,000 labelings, 1,000 x 0.95 = 950, so the 950th largest max STCS is the significance threshold: for the correctly labeled data the max STCS is 3,101 voxels.
Only five labelings yield max equal to or larger than 3,101, so the P-value for the experiment is 5/1,000 = 0.005. The 95th percentile is 462, so any suprathreshold clusters with size greater
than 462 voxels can be declared significant at level 0.05. Two cluster with 3,101 and
1,716 voxels in size, with P-values of 0.005 and 0.015, respectively.

## Slide 5
Nichols & Holmes, HBM, 2001
Critical threshold of nonparametric test is 8.40.
For a t-statistic image of 43,724 voxels of size 2 x 2 x 4 mm, with an estimated smoothness of 7.8 x
8.7 x 8.7 mm, the parametric theory gives a 5% level critical threshold of 11.07 significantly higher than the corresponding nonparametric threshold.

## Slide 6
Nichols & Holmes, HBM, 2001
The null sampling distribution (given the data), is the permutation distribution of the maximal statistic computed over all voxels in the volume of interest, potentially including voxels
where the null hypothesis is not true. A large departure from the null hypothesis will give a large statistic, not only in the actual labeling of the experiment, but also in other labelings, particularly those close to the true labeling.
This does not affect the overall validity of the test, but may make it more conservative for
voxels other than that with the maximum observed statistic. One possibility is to consider step-down tests, where significant regions are iteratively identified, cut out, and the remaining volume reassessed. The resulting procedure still maintains strong control over family-wise Type I error, our criteria for a test with localizing power, but will be more powerful (at voxels other that with maximal statistic).

## Slide 7
Nichols & Holmes, HBM, 2001
The iterative nature of the procedure, however, multiplies the computational burden of an already intensive procedure. Holmes et al. (1996) give a discussion and efficient algorithms, developed further in Holmes (1994), but find that the additional power gained was negligible for the cases studied.

## Slide 8
Nichols & Holmes, HBM, 2001
We can calculate such statistic for each voxel.
=> Multiple Comparison Problem (MCP)
For the single threshold test to be equally sensitive at all voxels, the (null) sampling distribution of the chosen statistic should be similar across voxels. For instance, the
simple mean difference statistic used in the single voxel example could be considered as a voxel statistic, but areas where the mean difference is highly variable will dominate the permutation distribution for the maximal statistic. The test will still be valid, but will be less sensitive at those voxels with lower variability. So, although for an individual voxel a permutation test on group mean differences is equivalent to one using a two-sample t-statistic (Edgington, 1995), this not true in the multiple comparisons setting using a maximal statistic

## Slide 9
Holmes, Blair, Watson & Ford, Journal of Cerebral Blood Flow and Metabolism, 1996
An additional cause for concern is the observation that an activation that dominates the statistic image will raise the observed maximal statistic above what it might be, were there no activation. Such a strong activation will influence the statistic images for the relabellings, particularly those for which the labelling is close to that of the experiment, possibly dominating the relabelled statistic image and hence leading to higher randomisation values than were there no activation. Thus, strong activation can increase the critical value of the test.

## Slide 10
Increasing amplitude and increasing smoothness
with increasing latencies of event related potentials / fields

## Slide 11
Maris & Oostenveld, 2007

## Slide 12
Maris & Oostenveld, 2007

## Slide 13
Nonparametric analysis of simulated EEG data
in condition A
Assumed 15 subjects
Paired t-test:
t(14)=3.156; p=0.007
F=t2=9.96
in condition B

## Slide 14
ERPs: early, short and small + later, longer and bigger

## Slide 15
Synthetic topographies multiplied by subject/condition

## Slide 16
Paired t-test of synthetic topographies without noise

## Slide 17
Cluster permutation of no-noise data:
late cluster only survives permutation
with whole time interval analysis

## Slide 18
Cluster permutation of no-noise data
with specific investigation
of early time interval enables detection
of early cluster

## Slide 19
Cluster permutation of no-noise data
with whole time interval
but sequential rejection enables detection
of early cluster

## Slide 20
Cluster permutation of no-noise data
with whole time interval
and a piori focus on anterior sensors
also enables detection of early cluster
c

## Slide 21
ERPs with white noise: 5%, 10% or 15% of maximum

## Slide 22
Paired t-test of ERPs with 5% max. noise

## Slide 23
Cluster permutation of 5% noisy data:
late cluster only survives permutation
with whole time interval analysis

## Slide 24
Cluster permutation of 5% noisy data
with specific investigation
of early time interval enables detection
of early cluster

## Slide 25
Cluster permutation of 5% noisy data
with whole time analysis
but sequential rejection
enables detection of early cluster

## Slide 26
Cluster permutation of 5% noisy data
with whole time analysis
and a-priori focus on anterior sensors
also enables detection of early cluster
c

## Slide 27
Cluster permutation of 10% noisy data:
late cluster only survives permutation
with whole time interval analysis
Early cluster not sig. on 0.05 first level

## Slide 28
Cluster permutation of 10% noisy data:
late cluster only survives permutation
with whole time interval analysis
Early cluster sig. on 0.1 first level

## Slide 29
Cluster permutation of 10% noisy data:
late cluster only survives permutation
with whole time interval analysis
Early cluster sig. on 0.1 first level
Sequential rejection lowers critical cluster mass
but still not sufficient to get early cluster sig.

## Slide 30
Cluster permutation of no-noise ANOVA
data with whole time analysis
also enables detection of early cluster
c
F=t2=9.96

## Slide 31
Cluster permutation of 5% noisy ANOVA
data with whole time analysis
also enables detection of early cluster
c
F=t2=9.96

## Slide 32
Cluster permutation of 10%
noisy ANOVA data
late cluster only survives permutation
with whole time interval analysis
c
F=t2=9.96

## Slide 33
Cluster permutation of 10%
noisy ANOVA data and sequential rejection
early clusters survives permutation
with whole time interval analysis
c
F=t2=9.96

## Slide 34
This „latency bias“ - i.e. masking of smaller cluster by dominating
bigger cluster - depends on relative length, relative amplitude
of small versus big cluster as well as S/N

## Slide 35
The step-down test described here is a sequentially rejective test (see Holm, 1979), adapted to the current application of randomisation testing. Starting with the intracerebral voxels, the p value for the maximal statistic is computed as described. If this p value is greater than a, the omnibus hypothesis is accepted. Otherwise, the voxel with maximum statistic is declared as activated and the test is repeated on the remaining voxels, possibly rejecting the null hypotheses for the voxel with maximal value in this reduced set of voxels. This is repeated until a test rejects no further voxel hypothesis, at which stage the sequence of tests stops. Thus, activated voxels are identified, cut out, and the remainder of the volume of interest analysed, the process iterating until no more activated voxels are found.
From:
Nonparametric Analysis of Statistic Images from Functional Mapping Experiments A. P. Holmes, *R. C. Blair, HJ. D. G. Watson, and I. Ford
Holm S (1979) A simple sequentially rejective multiple test procedure. Scand J Statist 6:54--70

## Slide 36
In case of extreme differences in cluster sizes and/or small S/N even the step down procedure might not suffice as the corona around the significant cluster might still dominate the image.
In this case one could reduce the corona size:
Increase the extension of the mask of the previous cluster by using a reduced significance threshold e.g. cluster level p < 0.05 but cluster rejection level p < 0.2 (here Sequential Rejcetion Factor = 4)